## Slide 1
Notes on Blocked Dense Matrix Multiply example
written in BSV using BClib
for Convey Platforms
Rishiyur S. Nikhil
Bluespec, Inc.
September 3, 2013
© Bluespec, Inc., 2013
www.bluespec.com

## Slide 2
Introduction
This document provides some explanatory notes on an example “Blocked Dense Matrix Multiply” code for Convey platforms, written in the BSV language and using Bluespec’s BClib library for Convey platforms.
The purpose of this example is to illustrate how to write codes with complex memory access patterns using BSV/BClib. Optimization of the core arithmetic is a separate problem, and has not yet been addressed here.
  Currently it works on matrices of 64-bit signed integers, and the core BlockMAC is quite serial. It would be easy to substitute other 64-bit arithmetic such as floating point, fixed-point, complex, or other). The BlockMAC also needs to be parallelized for better performance. See additional notes at end of this document.
This example is very flexible with respect to memory layout of the input and output matrices, memory layout of blocks within these matrices, etc.

## Slide 3
Matrix multiplication basics
m
n
p
n
p
m
j
i
i
j
k
k
X
=
C
A
B
C = A x B
Each element Cij =
inner_product (row Ai,
column Bj)
for (i = 0..m-1)
for (j = 0..p-1)
C[i,j] = 0;
for (k = 0..n-1)
C[i,j] = C[i,j] + A[i,k] x B[k,j]
In this doc, and in the BSV code, we strictly follow certain variable-naming conventions, as shown in the diagram above:
m, n, p for dimensions of A, B and C
I, j, k for indexes along the m, p and k dimensions, respectively
“inner product”
“multiply-accumulate” a.k.a. “MAC”

## Slide 4
“Blocked” Matrix multiplication (“BMM”)
mb
nb
p
n
p
m
j
i
i
j
k
k
X
=
Instead of iterating over individual rows and columns of scalars, we iterate over “blocks” of rows and columns.
mm, nn, pp: dimensions of blocks in A, B and C (see figure above)
Each inner-product, therefore, involves
“multiplication” of (mm x nn) blocks from A with (nn x pp) blocks from B
“addition” of “(mm x nn)” blocks (blocks of C)
Here “multiplication” and “addition” are, simply, matrix multiplication of scalars and matrix addition of scalars (unblocked).
Why? If a processor reads entire blocks into “local” memory and performs block multiplications and additions locally, the total number of main memory references can be reduced (by a factor of the block size), which can improve overall performance.
mm
nn
nn
pp

## Slide 5
BMM for Convey: top-level parallelization
For the top level of parallelization, one option is to simply slice the A and C matrices horizontally into four parts, so that:
FPGA 0 does: C0 = A0 x B
FPGA 1 does: C1 = A1 x B
FPGA 2 does: C2 = A2 x B
FPGA 3 does: C3 = A3 x B
Each of these is just an independent matrix multiplication, so all FPGAs can have the same hardware setup; we just provide them with different matrix addresses on startup.
This code will equally well support other parallelizations, such as slicing B and C vertically into four parts (see later slide on “input arguments”).
X
=
A0
A1
A2
A3
C0
C1
C2
C3

## Slide 6
BMM for Convey: each FPGA
mkMatrixMult
“vips” (N_engines <= 8 (parameter))
mkInnerProduct
mkblock_MAC
mkScalarMAC
rl_distribute_task_to_engine
rl_distribute_task_to_engine
rl_argv_request
rl_argv_response
rl_init_vips
(with mm, nn, pp, nb, addr incrs)
rl_gen_vip_tasks
rl_all_done
8 MCs (Convey memory ports)
mkInnerProduct
mkblock_MAC
mkScalarMAC
Each mkInnerProduct engine is attached to one Convey MC even/odd pair. The argv request/response rules use the last (MC 7) even/odd pair briefly, at the start of the computation.
rl_wait_for_completion

## Slide 7
BMM for Convey: each InnerProduct engine
mkInnerProduct
mkblock_MAC
mkScalarMAC
rl_reqs_A
rl_resps_A
rl_reqs_B
rl_resps_B
mkCompletionBuffer2
cb_rsps_e
mkCompletionBuffer2
cb_rsps_o
rl_C_block_writer
An even
MC port
An odd
MC port
read nb blocks,
each mm x nn
read nb blocks,
each nn x pp
Manage
memory
ordering
getC
read 1 block,
mm x pp
(alternate even and odd MC ports)
rl_init_c_block
putA
putB
zero out c_block
a_block
b_block
c_block
Buffers to hold a block of A, B and C
rl_join
rl_MAC_i1_j1_loop
rl_MAC_i1_j1_loop_step2
rl_MAC_k1_loop
put_a_b
get_c
pipelined
c = c + a x b
rg_c
rl_completion

## Slide 8
BMM for Convey: memory layout independence
mb
nb
p
n
p
m
j
i
i
j
k
k
X
=
mm
nn
nn
pp
The code can be used with many possible memory layouts for the matrices, because it takes arguments specifying the following (we do not assume square matrices or blocks):
argument | Offset in arg block | comment
pA, pB, pC | [1], [2], [3] | Address of A[0,0], B[0,0], C[0,0]
mb, nb, pb | [4], [5], [6] | # of blocks in m, n and p dimensions
mm, nn, pp | [7], [8], [9] | Block sizes A:mmxnn, B:nnxpp, C:mmxpp
dAi1, dAk1, dAib, dAkb | [10], [11], [12], [13] | Address increment for A, by 1 row, 1 col, by mb rows, by nb cols
dBk1, dBj1, dBkb, dBjB | [14], [15], [16], [17] | Address increment for B, by 1 row, 1 col, by nb rows, by pb cols
dCi1, dCj1, dCib, dCjb | [18], [19], [20], [21] | Address increment for C, by 1 row, 1 col, by mb rows, by pb cols
Note: this supports, independently:
Row-major or column-major ordering of blocks
Row-major or column-major ordering of elements within blocks
Padding between elements, padding between blocks
Different layouts for A, B, and C
Non-square, non-power-of-2-size matrices and blocks
etc.

## Slide 9
BMM for Convey: input arguments
The host software prepares the matrices, and passes these arguments to the FPGAs in an arg block, which is an array of 1024 64-bit words, 256 per FPGA.
The arguments can in principle be completely different for each FPGA. If we divide work across FPGAs by horizontally slicing A and C, only pA and pC will be different for the different FPGAs. If we divide work by vertically slicing B and C, only pB and pC will be different.
We only have 22 args for each FPGA, so a 256-word array for each FPGA is overkill, but this part of the code can be reused as-is for different apps with different # of args.
The single argument to the top-level mkApp_HW module in all four FPGAs is a pointer to this block.
This module, in turn, calls its mkMatrixMult.start() method with the pointer + (FPGA_id << 11), which points at the 256-word block for current FPGA.

## Slide 10
BMM for Convey: notes
Synthesis results (for Convey HC-1ex)
N_engines = 8 (per FPGA); signed 64-bit integer arithmetic
Resource utilization: LUTs 23%, Registers 14%, DSPs 9%, Block RAMS: 4%
  So: there is plenty of space for optimization of the core arithmetic, BlockMAC and ScalarMAC
Zero timing errors (no negative slack)
The current mkScalarMAC block has a naïve integer multiplication, with too many stages. Instead, this should just use a wrapped version of an existing optimized core, from Xilinx or elsewhere.
Currently, the inner conventional matrix-multiply of two blocks, inside mkBlock_MAC, is sequential. This should be parallelized (e.g., using a systolic array).
To convert to floating-point arithmetic, simply substitute the mkScalarMAC block
Synthesis notes:
When doing a ‘make’ to compile the bitfile, in Personality/Makefile.include,
  set MC_XBAR=1
  set MC_READ_ORDER=1
Before doing ‘make’ to create the bitfile, first do ‘make cae_fpga.xst’, and edit the cae_fpga.xst file to change the following Xilinx options:
  -fsm_extract YES => NO
  -resource_sharing YES => NO
  -equivalent_register_removal YES => NO